## Slide 1: Santo Village, Haiti Compost-Based Toilet System
5th International Dry Toilet Conference
Tampere University of Applied Sciences
19th – 22nd of August, 2015
Joseph Jenkins, Inc.
EcologicalSanitation.com

## Slide 2: Nature suggests that we bury odorous things.

## Slide 3
We bury corpses.
We deposit fecal material
into holes in the ground.

## Slide 4
Science shows us a new way to bury organic material.

## Slide 5
Instead of burying with dirt, we can bury with materials derived from plants.

## Slide 6
When we bury odorous organic materials with plant material, we promote the growth of heat producing bacteria.

## Slide 7
The resulting organic mass, called a compost pile, destroys human disease organisms.
Researchers include Gotaas, (1956 W.H.O.); Feachem, et al. (1980 World Bank). Franceys, R. et al. (1992 W.H.O.) and others.

## Slide 8
This is the basis of sanitation and
the promotion of public health.

## Slide 9
“Composting”
by definition, is
Managed
Aerobic
3) Produces biological heat

## Slide 10
Most “dry toilets” are erroneously called “composting” toilets, but they do not compost. They dessicate, dehydrate, and decompose the toilet material.

## Slide 11: Organic materials, including toilet materials, are composted simply by:
COLLECTING IN CONTAINERS
PILING IN COMPOST BINS
COVERING WITH PLANT MATERIAL

## Slide 12: Compost toilets collect all toilet materials, including urine and toilet paper.

## Slide 13
Here, a 20-liter receptacle under the toilet seat collects the feces, urine and paper.
Urine separation is not necessary when the collected material is being composted.

## Slide 14: The contents are covered with the carbon-based plant material, which acts as a biofilter to prevent odor. The receptacle is easily removable.

## Slide 15: The Santo Village in Leogane, Haiti, was a Habitat for Humanity planned Village for displaced families.

## Slide 16: Jimmy Carter even worked at the site.

## Slide 17: Their first sanitation choice was the Otji dry toilet, a urine separating, dehydrating toilet.

## Slide 18: The expensive OTJI system failed, primarily due to odors, management issues, and environmental threats. GiveLove.org then set up a true compost sanitation system in the Village.

## Slide 19: True Composting Step 1: Collect the organic material.

## Slide 20: Step 2: Obtain appropriate cover material.

## Slide 21: Step 3: Pile the organic material in bins. Start by training.

## Slide 22: Bins can be built with recycled pallets. Begin with a “biological sponge.”

## Slide 23: Each compost bin had its own label.

## Slide 24: Toilet material is layered by the trained team, using bagasse as cover material.

## Slide 25: Compost receptacles need to be rinsed. The water is deposited into the bins.

## Slide 26: 250 households fill a 10 cubic meter bin every month.

## Slide 27: The village has two compost sites; both are fenced and locked.

## Slide 28: Toilet material is collected twice a week. Users bring their full receptacles to the compost yards and swap them for clean ones.

## Slide 29: This compost system requires no turning.

## Slide 30: A compost shed at each site stores tools and equipment.

## Slide 31: After a minimum of nine months, a beautiful, sanitary compost is produced. There is no odor.

## Slide 32: Public education helps to improve acceptance of this revolutionary sanitation system.

## Slide 33: Instructions are posted inside each toilet.

## Slide 34: Composting recycles organic material. There is no waste, no pollution, and no disposal.

## Slide 35
The Santo Village project was created by GiveLove.org:
Patricia Arquette (Founder),
Alisa Keesey (Program Director),
Jean Lucho (Compost Instructor)
GiveLove.org is now working in
Nicaragua and India.

## Slide 36: Download the full, illustrated paper on the Santo Village compost sanitation project:
humanurehandbook.com/downloads/Santo_Paper.pdf
QUESTIONS?
Presentation by Joe Jenkins
Joseph Jenkins, Inc., USA
EcologicalSanitation.com
joecjenkins@gmail.com